## Slide 1
Background
Research
Results
Experiments
Target Vehicle Middle size fuel cell hybrid vehicle
Development of energy management strategy for PEMFC-HEV considering
degradation of fuel cell system
송창희1) · 조구영2) · 차석원1)
1)서울대학교 기계공학과, 2)단국대학교 기계공학과
Research Background
A. Increased importance of fuel economy due to emission regulations
Electrification of the vehicles is accelerating
There is increasing interest in efficient fuel cell vehicles without emitting exhaust gas
B. Necessity of developing power distribution strategy (PDS) that guarantees generalization performance for Fuel Cell Hybrid Electric Vehicles (FCHEVs)
Optimal control theories have developed PDS considering future information
Since reinforcement learning (RL) derives a PDS considering only the current state, there is a growing interest in PDS for HEVs using the RL
C. PDS considering the deterioration of fuel cells
Since fuel cells are vulnerable to deterioration, it is necessary to develop the PDS that considers deterioration.
DC/AC
+
-
DC/DC
Deep Reinforcement Learning
  DRL is composed on the Markov Decision Process (MDP) Framework consisting of an agent and an environment
  In this study, we approach the DRL problem using the Actor-Critic algorithm
  Definition of state, action, and reward:
    State 
    Action 
    Reward 
Research Objectives
PDS for FCHEVs development using deep reinforcement learning
B. PDS for FCHEVs development that guarantees generalization performance
C. Control Strategy development considering the fuel cell deterioration
Battery
Motor
FC stack
FCHEV 동향 등
Properties | Values
Maximum stack power [kW] | 67
Maximum battery power [kW] | 40
Vehicle mass [kg] | 1200
Tire radius [m] | 0.337
Final gear ratio | 3.648
Initial SOC | 0.6
Validation Test with ECMS (Equivalent Consumption Minimization Strategy)
  When all driving information is given, the ECMS shows a performance close to the global optimum
  We test the validity of the AC model through ECMS results given all driving information.
  We confirm that our model shows results corresponding to ECMS